## Slide 1: TherMOS: A Toolkit for Low Resolution Thermal Modeling
Dr. Pascal Schirmer

## Slide 2: Version History
# | Version | Date | Comment | Editor | Lead
1 | v.1.0 | 15.05.2025 | Creating initial version. | Pascal Schirmer | Pascal Schirmer

## Slide 3: Content
Short Introduction
Theoretical Background
Toolkit Overview
Exemplary Calculation
Advanced Functionalities
Outlook and Conclusion

## Slide 4: A
Short Introduction

## Slide 5: Aims and Goals
This MATLAB script/toolkit focuses on the reduction of high-order thermal models to more manageable lower-order models while preserving essential thermal dynamics. Thermal model order reduction is critical in simulations and real-time control applications where computational efficiency and accuracy are paramount. This process is typically necessary for systems with many thermal nodes, where full-scale modeling would be computationally prohibitive.

## Slide 6: Dependencies
Used Hardware
OS: WIN 10
CPU: AMD 3700X
RAM: 32 GB 3600 MHZ DDR4
ROM: 1 TB SSD
GPU: NVIDIA RTX 3700
Software
The TherMOS Toolkit was implemented using Matlab R2023b and the following toolbox:
distrib_computing_toolbox
identification_toolbox
image_toolbox
matlab
neural_network_toolbox
optimization_toolbox
statistics_toolbox

## Slide 7: Limitations and Known Issues
Numerical discrepancies for default implementation for calculating Gth and Cth matrices for 2D POD method
Thermal structure function has convergence issues (should currently not be used)
Deep learning does not support sequence-to-sequence learning

## Slide 8: B
Theoretical Background

## Slide 9: B1
Fundamentals of Thermal model order Reduction

## Slide 10
Literature:
Images:
Software:
Example:
Content:

## Slide 11: B1
Fundamentals of Thermal model order Reduction

## Slide 12: C
Toolkit Overview

## Slide 13: Toolkit Overview
Overview
Description
The toolkit implements model order reduction methods for 1D and 2D thermal problems
The main contribution of the toolkit is the implementation of the proper orthogonal decomposition (POD) using a Galerkin and a state space approach
1D Foster networks and state space systems provide reference setups for simple approaches commonly used in industry
Fundamentals of machine and deep learning are implemented as well
Literature: -
Images: -
Software: TherMOS
Example: -
Content: Toolkit Description

## Slide 14: Installation and Usage
Step I:
Check out Github
Clone the latest version of the TherMOS Toolkit from Github: https://github.com/pascme05/TherMOS
Step II:
Install MATLAB
Install Matlab R2023b or higher to ensure the toolkit to run smoothly.
https://de.mathworks.com/help/install/ug/install-products-with-internet-connection.html
Step III:
Run start.Mat
To execute a new simulation three things are needed. First, a valid configuration file. Second, a training and testing dataset. Third a start script as provided in start.mat used for defining the configuration and the datasets.
Literature: -
Images: -
Software: TherMOS
Example: -
Content: Toolkit Description

## Slide 15: Project Structure
TherMOS | Folder | Subfolder | Content
¦-- | config |  | Contains the configuration files
¦-- | data |  | Contains the datasets for training and testing
¦-- | docu |  | Contains the documentation
¦-- | gen |  | Contains code for generation of exemplary data
¦-- | mdl |  | Contains trained models
¦-- | results |  | Contains all results
¦-- | setup |  | Contains preconfigured setup sheets
¦-- | src |  | Contains source code implementation
 | ¦-- | data | Contains functions for loading data
 | ¦-- | dev | Contains functions for electrical calculation
 | ¦-- | general | Contains general and helper functions
 | ¦-- | model | Contains functions for reduced order models
 | ¦-- | numeric | Contains functions for numerical integration
 | ¦-- | plot | Contains functions for plotting
Literature: -
Images: -
Software: TherMOS
Example: -
Content: Toolkit Description

## Slide 16: Setup File
Description
Experiment
  Define training and testing
  Define config file
Data Files
  Define data formats
  Define inputs and outputs
Models
  Activate analytical 1D/2D models
  Activate machine/deep learning
Literature: -
Images: -
Software: TherMOS
Example: -
Content: Toolkit Description

## Slide 17: Configuration File
Change Log
All changes to the templated are logged here
New config files should be based on the default file
Legend
Colour coding to indicate which cell should be changed an which not
Colour code is valid throughout all worksheets
Settings
Four worksheets to adapt: experiment, data, models, and parameters
Each worksheet as drop downs a limits for the values
Literature: -
Images: -
Software: TherMOS
Example: -
Content: Toolkit Description

## Slide 18: Data Files
Readme
General overview about the dataset structure
1D data description
2D data description
1D Matlab/Excel
1D timeseries can be defined in Excel or Matlab
The format uses T samples, for M inputs and N outputs
2D Matlab
2D spatial and temporal varying problems can be defined in Matlab only
The format uses T samples and MN spatial values
Literature: -
Images: -
Software: TherMOS
Example: -
Content: Toolkit Description

## Slide 19: D
Exemplary Calculations

## Slide 20: Problem Description: 1D Dataset
Physical Problem
Dataset Description
The data contains heat up curves for a transformer with E core
  Input: Losses for primary, secondary, and core
  Output: Temperatures for primary, secondary, and core
The winding and the core are thermally coupled
The amount of coupling depends on the operating point
Three operating points are included (OP1-OP3)
Primary
Winding
Secondary
Winding
Transformer
Core
Literature:
Images:
Software:
Example:
Content:

## Slide 21: Problem Description: 2D Dataset
Physical Problem
Dataset Description
Copper
Dielectric
Aluminium
Thermal Interface Material
The dataset contains thermal data from an insulated metal substrate board (IMS) [1]
  Losses from two power semiconductor switches
  Convective boundary at the bottom
  Adiabatic on all other edges
The switches are coupled through the copper layer
The dominant heat flux is in direction of the cooling
h [µm] |  |  | 
100 | 8933 | 400 | 380
50 | 2200 | 2 | 800
1500 | 2680 | 90 | 1000
500 | 3300 | 4 | 1500
h [µm] |  |  | 
100 | 8933 | 400 | 380
50 | 2200 | 2 | 800
1500 | 2680 | 90 | 1000
500 | 3300 | 4 | 1500
Literature:
Images:
Software:
Example:
Content:

## Slide 22: Problem Description: ML/DL Dataset
Physical Problem
Dataset Description [2]
The dataset contains ~180 hrs of measured testbench data for an electric machine (PSM)
  Input: Currents, Voltages, torque, speed, etc.
  Output: Stator and Rotor temperatures
The dataset is cluster in IDs for splitting training, testing and validation
Dataset made publicly available from Paderborn University: [4]
[2,3]
Literature:
Images:
Software:
Example:
Content:

## Slide 23: D1
Analytical 1D Model order Reduction

## Slide 24: RC-Model: Training and Testing Results
Settings & Parameters
Steady & Trans. Error Metric
Testing Data Plot
Chart: time [sec]
Chart: time [sec]
 | MAE | MSE | MAX
SS | 18,55 | 364,5 | 22,70
TR | 3,17 | 13,05 | 5,96
All | 17,32 | 336,3 | 22,70
Fixed model order 3
Foster structure
Training OP1, Testing OP2
 | Node-1 | Node-2 | Node-3
 | 1,60 | 2,40 | 0,36
 | 60,1 | 130,6 | 24,3
 | Node-1 | Node-2 | Node-3
 | 1,60 | 2,40 | 0,36
 | 60,1 | 130,6 | 24,3
Chart: Transient Thermal Impedance
| 1E-3 | 2E-3 | 5.0000000000000001E-3 | 0.01 | 0.02 | 0.05 | 0.1 | 0.2 | 0.5 | 1 | 2 | 5 | 10 | 20 | 50 | 100 | 200 | 500 | 1000 | 2000 | 5000 | 10000
Z_th_T | 6.5446e-05 | 0.00013089 | 0.00032718 | 0.00065424 | 0.001308 | 0.0032663 | 0.0065204 | 0.012992 | 0.032122 | 0.063085 | 0.12177 | 0.27578 | 0.47861 | 0.77221 | 1.3614 | 2.05 | 2.8922 | 3.8643 | 4.2612 | 4.3559 | 4.36 | 4.36
Literature:
Images:
Software:
Example:
Content:

## Slide 25: SS-Model: Training and Testing Results
Settings & Parameters
Steady & Trans. Error Metric
Testing Data Plot
Training: OP1/3, Testing: OP2
Model Order: 2
Inputs: Primary, secondary, and core losses
Model form: Continuous
Noise modeling: off
Solver: linear
Chart: time [sec]
SS | MAE | MSE | MAX
Pri | 1,98 | 3,93 | 2,23
Sec | 2,05 | 4,33 | 3,06
Core | 1,35 | 2,62 | 2,53
Chart: time [sec]
TR | MAE | MSE | MAX
Pri | 2,06 | 4,80 | 2,71
Sec | 1,69 | 3,72 | 3,02
Core | 0,71 | 0,58 | 1,06
Literature:
Images:
Software:
Example:
Content:

## Slide 26: RC- and SS-Model Comparison
Error Comparison Secondary (OP2)
Description &
Analysis
State Space system outperform RC networks for MAE, MSE, and MAX error
The losses in the transformer are coupled, thus primary, secondary and core losses mutually influence the temperature
RC networks cannot predict the temperature accurately due to the coupling
State Space models include the thermal coupling resistances and the power mapping inside their state space matrices
Chart: time [sec]
 | MAE | MSE | MAX
SS | 2,02 | 4,28 | 3,06
RC | 17,32 | 336,3 | 22,70
Literature:
Images:
Software:
Example:
Content:

## Slide 27: D2
Analytical 2D Model order Reduction

## Slide 28: POD-Model: Training Spatial Modes
Training based on one step response with 5 W losses (2,84E8 W/m³)
Using fixed number of POD modes equal to three
Using ode23s as stiff solver for Gth and Cth system
Using Gaussian Legendre Integration and Jacobi matrix for mesh correction
Literature:
Images:
Software:
Example:
Content:

## Slide 29: POD-Model: Testing Spatial Error X
Both temperature and gradient are well captured
Largest temperature error at boundary interface
Largest gradient error at points of gradient changes
Literature:
Images:
Software:
Example:
Content:

## Slide 30: POD-Model: Testing Spatial Error Y
Gradient is directly proportional to the heat conductance of the PCB materials
Temperature error increase in direction of the heat sources
Literature:
Images:
Software:
Example:
Content:

## Slide 31: POD-Model: Testing Temporal Error
Temporal behaviour is captured well
Maximum error around 1,0 K
Steady state error around 0,2 K
Literature:
Images:
Software:
Example:
Content:

## Slide 32: D3
Deep Learning 1D Model order Reduction

## Slide 33: DL-CNN: Training and Testing Results
Settings & Parameters
Normalisation X,y: off
Learning rate: 0,001
Batch: 1024
Input window: 600
Max Epochs: 100
Layer Structure
  2x CNN ([5,64], [3,32])
  1x DNN (32 nodes)
Steady & Trans. Error Metric
 | MAE | MSE | MAX
T_sw | 5,34 | 45,7 | 17,8
T_st | 3,48 | 49,9 | 11,6
T_so | 3,38 | 25,0 | 17,3
T_rm | 6,12 | 53,0 | 20,2
Avg | 4,58 | 35,9 | 20,2
Testing Data Plot
Chart: time [sec]
Literature:
Images:
Software:
Example:
Content:

## Slide 34: DL-LSTM: Training and Testing Results
Settings & Parameters
Normalisation X,y: off
Learning rate: 0,001
Batch: 1024
Input window: 600
Max Epochs: 100
Layer Structure
  1x LSTM (64 nodes)
  1x DNN (64 nodes)
Steady & Trans. Error Metric
 | MAE | MSE | MAX
T_sw | 3,29 | 18,4 | 26,9
T_st | 2,23 | 9,37 | 22,4
T_so | 1,92 | 6,47 | 17,0
T_rm | 7,28 | 69,0 | 21,8
Avg | 3,68 | 25,8 | 26,9
Testing Data Plot
Chart: time [sec]
Literature:
Images:
Software:
Example:
Content:

## Slide 35: DL-Model Comparison
Error Comparison Stator Winding (ID60)
Description &
Analysis
LSTM outperforms CNN for MAE and MSE, but shows significantly higher MAX error
CNN generate smoothing effect through convolution
LSTM accurately models temporal behaviour
Chart: time [sec]
 | MAE | MSE | MAX
CNN | 5,34 | 45,7 | 17,8
LSTM | 3,29 | 18,4 | 26,9
Literature:
Images:
Software:
Example:
Content:

## Slide 36: E
Advanced functionalities

## Slide 37: E1
Advanced functionalities: POD State Space Model

## Slide 38: POD-SS Model
Instead of calculating Cth and Gth matrices, a state space system is used to model the temporal dependencies
Improved transient modeling for low spatial and temporal resolution
Max error reduces from -1,0 K to -0,65 K
Literature:
Images:
Software:
Example:
Content:

## Slide 39: E2
Advanced functionalities: Deep Learning

## Slide 40: Optimised Neural Network Architecture
Error Comparison Stator Winding (ID60)
Description &
Analysis
Combining a CNN and LSTM based architecture to utilise temporal and spatial convolution characteristics
Significant further improvement for all error metric
Chart: time [sec]
 | MAE | MSE | MAX
CNN | 5,34 | 45,7 | 17,8
LSTM | 3,29 | 18,4 | 26,9
Opti | 2,80 | 13,4 | 13,5
Literature:
Images:
Software:
Example:
Content:

## Slide 41: Optimised Features and Neural Network Architecture
Error Comparison Stator Winding (ID60)
Description &
Analysis
Adding additional input features, e.g. torque and rotational speed
Further improvement in all error metric
Lowest overall error
 | MAE | MSE | MAX
CNN | 5,34 | 45,7 | 17,8
LSTM | 3,29 | 18,4 | 26,9
Opti | 2,80 | 13,4 | 13,5
Opti2 | 2,37 | 9,43 | 10,2
Chart: time [sec]
Literature:
Images:
Software:
Example:
Content:

## Slide 42: F
Outlook and Conclusion

## Slide 43: Development and Future Goals
As failure and mistakes are inextricably linked to human nature, the toolkit is obviously not perfect, thus suggestions and constructive feedback are always welcome. If you want to contribute to the TherMOS toolkit or spotted any mistake, please contact me via: p.schirmer@herts.ac.uk. The following aspects will be improved in future version:
3D input files for the Proper Orthogonal Decomposition (POD)
Physics Informed Neural Networks (PINNs) for 1D and 2D problems

## Slide 44: G
References

## Slide 45: Bibliography
[1] https://www.ventec-group.com/products/tec-thermal-thermal-management-ims/vt-4b3/datasheet/
[2] W. Kirchgässner, O. Wallscheid and J. Böcker, "Estimating Electric Motor Temperatures With Deep Residual Machine Learning," in IEEE Transactions on Power Electronics, vol. 36, no. 7, pp. 7480-7488, July 2021, doi: 10.1109/TPEL.2020.3045596
[3] https://github.com/upb-lea/deep-pmsm
[4] https://www.kaggle.com/datasets/wkirgsn/electric-motor-temperature
[5]